## Slide 1: Hourly Power Data
European wholesale power — prices, generation & capacity
17 July 2026
ENTSO-E hourly data · auto-linked workbook

## Slide 2: Price volatility & negative-price hours
Annual volatility and the incidence of negative prices across the five markets
Source: ENTSO-E Transparency Platform (hourly prices, generation, flows & capacity).
Price volatility: annual SD of hourly day-ahead price (€/MWh)
Negative-price hours per year, by country
Chart: EUR/MWh
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Germany | 15.52 | 17.5 | 73.68 | 142.82 | 47.58 | 52.73 | 52.09
Spain | 10.88 | 11.42 | 74.71 | 69.46 | 41.34 | 45.94 | 47.61
Portugal | 10.81 | 11.26 | 74.7 | 69.13 | 39.93 | 45.57 | 46.44
France | 14.02 | 16.11 | 84.31 | 145.84 | 45.53 | 40.66 | 46.38
Italy | 12.67 | 14.63 | 81.08 | 133.15 | 35.59 | 29.66 | 29.69
Chart: # hours
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Germany | 211 | 298 | 139 | 70 | 300 | 457 | 576
Spain | 0 | 0 | 0 | 0 | 0 | 247 | 556
Portugal | 0 | 0 | 0 | 0 | 0 | 196 | 200
France | 27 | 102 | 64 | 4 | 147 | 352 | 513
Italy | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 3: Negative & extreme prices in detail (Germany)
How negative-hour incidence builds through the year, and the daily price range
Source: ENTSO-E Transparency Platform (hourly prices, generation, flows & capacity).
Cumulative near-negative-price hours through the year (Germany)
Daily minimum vs maximum price (Germany, 2024)
Chart: # hours (cum)
Chart: max EUR/MWh

## Slide 4: Intraday price shape & price duration
Average intraday price profile by year, and the full price distribution
Source: ENTSO-E Transparency Platform (hourly prices, generation, flows & capacity).
Intraday price shape by year, indexed to daily mean (Germany)
Price duration curves by year (Portugal)
Chart: indexed (1=base)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
2019 | 0.7721 | 0.7461 | 0.7387 | 0.7738 | 0.9055 | 1.0721 | 1.1763 | 1.1559 | 1.092 | 1.0408 | 0.9913 | 0.9352 | 0.9051 | 0.9249 | 0.9734 | 1.0838 | 1.2255 | 1.3174 | 1.2799 | 1.1608 | 1.0661 | 0.9764 | 0.874 | 0.813
2020 | 0.7574 | 0.7187 | 0.7029 | 0.7458 | 0.8905 | 1.0666 | 1.1929 | 1.1741 | 1.087 | 1.0181 | 0.9603 | 0.8779 | 0.8265 | 0.8626 | 0.9492 | 1.1067 | 1.3113 | 1.4441 | 1.3655 | 1.1902 | 1.0817 | 0.9834 | 0.879 | 0.8075
2021 | 0.7706 | 0.7456 | 0.7413 | 0.7799 | 0.913 | 1.0695 | 1.1878 | 1.1647 | 1.0992 | 1.0419 | 0.9974 | 0.9344 | 0.896 | 0.9237 | 0.9899 | 1.1178 | 1.2771 | 1.3402 | 1.2612 | 1.1297 | 1.0279 | 0.9357 | 0.8442 | 0.8111
2022 | 0.8372 | 0.8143 | 0.81 | 0.8564 | 0.9875 | 1.1114 | 1.1791 | 1.1165 | 1.0175 | 0.9349 | 0.8741 | 0.8171 | 0.794 | 0.8391 | 0.9193 | 1.0711 | 1.2462 | 1.3545 | 1.3122 | 1.1945 | 1.1062 | 1.0077 | 0.9271 | 0.8721
2023 | 0.8402 | 0.8162 | 0.8094 | 0.8489 | 0.9863 | 1.1422 | 1.182 | 1.1216 | 0.9948 | 0.894 | 0.8147 | 0.7407 | 0.7126 | 0.7757 | 0.8939 | 1.0617 | 1.2757 | 1.4525 | 1.3938 | 1.2454 | 1.1294 | 1.034 | 0.951 | 0.8831
2024 | 0.8513 | 0.8299 | 0.8244 | 0.8705 | 1.0208 | 1.1649 | 1.19 | 1.0695 | 0.9075 | 0.7729 | 0.6775 | 0.6043 | 0.5981 | 0.6839 | 0.8611 | 1.1057 | 1.4067 | 1.6145 | 1.5878 | 1.3191 | 1.1483 | 1.0355 | 0.9563 | 0.8994
2025 | 0.9172 | 0.8967 | 0.9008 | 0.9477 | 1.0628 | 1.1869 | 1.2039 | 1.0825 | 0.871 | 0.7065 | 0.5853 | 0.5145 | 0.5226 | 0.6303 | 0.8081 | 1.0732 | 1.3794 | 1.5787 | 1.5373 | 1.3475 | 1.1921 | 1.087 | 1.0087 | 0.9592
2026 | 1.0233 | 1.0035 | 1.0045 | 1.0322 | 1.1164 | 1.1666 | 1.1353 | 0.9809 | 0.7877 | 0.627 | 0.4893 | 0.3853 | 0.3872 | 0.5126 | 0.7128 | 0.9842 | 1.2833 | 1.5412 | 1.6484 | 1.5017 | 1.3231 | 1.1916 | 1.1087 | 1.0595
Chart: EUR/MWh

## Slide 5: Intraday generation mix & price (Portugal, 2024)
Hourly generation by technology, with the wholesale price overlaid
Source: ENTSO-E Transparency Platform (hourly prices, generation, flows & capacity).
Intraday generation mix and price (Portugal, 2024)
Chart: MW
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
Nuclear | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lignite | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Hard coal | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gas | 461.6 | 457.6 | 455.7 | 455 | 468.7 | 485 | 523.9 | 555.7 | 557.8 | 543.5 | 538.7 | 537.6 | 541.7 | 550.2 | 563.4 | 593.5 | 643.1 | 693.7 | 712.1 | 719.5 | 708.6 | 640.8 | 554.2 | 487.9
Oil & other fossil | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Biomass | 362 | 361.7 | 362.1 | 361.7 | 360.5 | 360.5 | 360.2 | 360.2 | 359.8 | 359 | 358.4 | 358.5 | 359.2 | 358.3 | 357.4 | 357.3 | 358 | 358.6 | 360 | 361.1 | 361.2 | 361.5 | 361.5 | 361.8
Waste | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Geothermal | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Hydro run-of-river | 891.7 | 791.5 | 749.5 | 772.4 | 866.1 | 1033.7 | 1123.8 | 1059.7 | 935.2 | 812.7 | 710.5 | 646.6 | 613.5 | 605.7 | 616.8 | 686.6 | 855.2 | 1155.9 | 1444.4 | 1570.4 | 1503.7 | 1326.8 | 1152.9 | 1010
Hydro reservoir | 368.2 | 336.1 | 323.7 | 330.7 | 358.3 | 425.5 | 459.7 | 441.8 | 388.2 | 328.7 | 292.7 | 279.5 | 265.2 | 258.9 | 266.6 | 311 | 406.4 | 535.1 | 660.6 | 752.7 | 663.4 | 542.1 | 471.8 | 407.9
Hydro pumped (production) | 562.6 | 468.9 | 430.8 | 452.4 | 573.7 | 849 | 959.9 | 860.6 | 575.5 | 323.2 | 214.1 | 187.5 | 152.1 | 151.1 | 181.8 | 266.6 | 602.7 | 1185.4 | 1740.8 | 1964.2 | 1759.5 | 1355 | 986.3 | 719.1
Onshore wind | 1735.1 | 1735.9 | 1745.9 | 1748 | 1731.4 | 1720 | 1701.1 | 1633.4 | 1521 | 1417.1 | 1341.1 | 1310.5 | 1320.1 | 1359.5 | 1413.2 | 1473 | 1544.5 | 1605.5 | 1660.4 | 1715.6 | 1746.3 | 1745.7 | 1743 | 1741

## Slide 6: Capture price vs baseload by technology (Germany)
How each technology's realised (capture) price compares with time-weighted baseload
Source: ENTSO-E Transparency Platform (hourly prices, generation, flows & capacity).
Capture price vs baseload by technology (Germany)
Chart: % vs base
| Nuclear | Lignite | Hard coal | Gas | Oil & other fossil | Biomass | Waste | Geothermal | Hydro run-of-river | Hydro reservoir | Hydro pumped (production) | Onshore wind | Offshore wind | Solar | Marine | Other renewable | Other
2019 | 1.88 | 8.6 | 19.03 | 10.46 | 1.26 | 0.47 | 0.07 | 0.45 | -0.23 | 11.71 | 24.06 | -14.2 | -7.74 | -7.33 | 1.6 | 2.92
2020 | 2.99 | 17.39 | 29.81 | 16.74 | 1.83 | 0.27 | 1.02 | 0.36 | -0.51 | 18.58 | -0.24 | -19.34 | -8.62 | -19.56 | 2.2 | 4.22
2021 | 1.1 | 10.31 | 29.5 | 10.99 | -0.77 | 1.01 | 2.01 | 4.76 | -6.69 | 11.18 | 28.48 | -16.64 | -4.65 | -22.09 | 4.14 | 3.51
2022 | 1.69 | 6.6 | 15.27 | 9.13 | 1.61 | 0.08 | -0.38 | -3.8 | 0.45 | 20.16 | 27.07 | -28.51 | -17.4 | -5.59 | -2.15 | -0.42
2023 | 19.29 | 15.59 | 22.52 | 15.38 | 0.36 | 1.97 | 0.13 | 1.59 | -1.62 | 16.6 | 31.97 | -17.43 | -9.06 | -24.16 | 4.08 | 5.27
2024 | 16.3 | 20.64 | 20.94 | 1.86 | 2.51 | 0.45 | 2.11 | -0.48 | 28.44 | 44.68 | -17.78 | -9.05 | -41.12 | 0.89 | 6.27
2025 | 16.68 | 25.12 | 23.59 | 3.92 | 3.94 | 1.15 | 3.96 | 1.06 | 27.45 | 45.52 | -13.4 | -4.24 | -48.44 | 1.71 | 7.22

## Slide 7: Installed generation capacity by technology (Germany)
Installed capacity by technology, 2019–2025
Source: ENTSO-E Transparency Platform (hourly prices, generation, flows & capacity).
Installed generation capacity by technology (Germany)
Chart: MW
| Nuclear | Lignite | Hard coal | Gas | Oil & other fossil | Biomass | Waste | Geothermal | Hydro run-of-river | Hydro reservoir | Hydro pumped (production) | Onshore wind | Offshore wind | Solar | Marine | Other renewable | Other
2019 | 9516 | 21205 | 25293 | 31745 | 4356 | 7782.1 | 1707 | 41.8 | 4007.9 | 1309 | 9422 | 52945.6 | 6393 | 45435 | 0 | 444.6 | 1235
2020 | 8114 | 21067 | 22458.4 | 31793.1 | 4372.5 | 8033.6 | 1681.6 | 47.5 | 3994.7 | 1308.5 | 9421.5 | 53338.2 | 7503.7 | 48376.4 | 0 | 407.5 | 1557.8
2021 | 8114 | 20487 | 23499.4 | 32038.2 | 4184.4 | 8447.1 | 1660.6 | 43.9 | 3838.8 | 1308.5 | 9421.5 | 54666.2 | 7773.8 | 53537.9 | 0 | 420.3 | 1638.8
2022 | 4056 | 18544.3 | 18829.5 | 30648.7 | 3966.3 | 8378.9 | 1619.5 | 50.9 | 3684.5 | 1309 | 9379.2 | 55456.3 | 7786.8 | 58002.3 | 0 | 352.4 | 1678.8
2023 | 4056 | 17692 | 18559 | 33135 | 4083 | 8513.8 | 1933 | 55.6 | 3737.2 | 1345 | 9379 | 57741.6 | 8128.8 | 63366 | 0 | 384.2 | 1706
2024 | 18365 | 18411 | 37584 | 4118 | 8659.5 | 1832 | 54 | 3752.8 | 1392 | 9449 | 60048.6 | 8456 | 77015.6 | 0 | 356.4 | 1630
2025 | 15178 | 15951 | 38596.6 | 6913.8 | 8851 | 1887 | 46 | 3923 | 1459.8 | 9383.8 | 63403.2 | 9215 | 86951.6 | 0 | 399.7 | 13287.5